## Slide 1: Eyeriss v2
A Flexible Accelerator for Emerging Deep Neural Networks on Mobile Devices
AuthorS:
Yu-Hsin Chen, Tien-Ju Yang, Joel Emer, Vivienne Sze
TeaM Presenting :
The Convuluted

## Slide 2: Table of Contents
Motivation/Background
Proposed Architecture
Performance and Results
Conclusion
Q/A?

## Slide 3: Motivations For EYERISS V2
Resource Constraints on Mobile Devices
Limitations of Current DNN Accelerators

## Slide 4: Resource Constraints on Mobile Devices
Deep learning applications are moving to resource- and energy-constrained Mobile platforms.
This has led to the development of smaller, more compact models (Compact DNN’s/Sparse DNN’s) that depend on specialized hardware(Accelerators) to perform efficiently

## Slide 5: Limitations of Current DNN Accelerators
Traditional DNN accelerators designed for large DNNs struggle with the compact and sparse models used in mobile platforms due to the variations in layer shapes, sizes, and data sparsity.
Compact DNNs: These networks, characterized by diverse layer shapes and sizes (e.g., MobileNet), challenge traditional accelerators that rely on fixed data dimensions and data reuse patterns.
Sparse DNNs: DNNs with sparse weights and activations (often exceeding 90% sparsity) offer energy and speed improvements but introduce irregular access patterns, making efficient hardware design challenging.

## Slide 6: The OBjective
The motivation is to design a DNN accelerator, Eyeriss v2, which can process both sparse and compact DNNs directly in the compressed domain to achieve significant gains in both processing speed and energy efficiency, particularly on mobile devices

## Slide 7: Accelerator Architecture
Special configurable Network-on-Chip (NoC) design
  Flexible to handle a variety of compact DNNs
  Two level hierarchy to reduce wiring, space, and power
  Can route between PEs, GLB Buffer, and external memory
  Has different routing modes

## Slide 8: Accelerator Routing
Purpose of Routing
  To control how data flows between PEs and memory
  Most accelerator routing is fixed and not flexible
  Unicast (one connected source to one connected destination)
  Multicast (one source to multiple destinations or multiple sources to one destination)
  Broadcast (one source to all connected destinations)
Configurable Routing Design
  Eyeriss V2 can do unicast and multicast routing
  Clusters are connected together in a 2D mesh topology globally and each local cluster has different topology

## Slide 9: Examples of Routing Configurations

## Slide 10: Accelerator Processing Elements
PEs Split into Clusters
  Allows memory and routing to be split into separate clusters
  All PEs take iacts, weights, and psums as input
Extra Logic for Handling Sparsity
  Uses special hardware logic to skip over 0s in PEs
  Hardware logic based on special sparsity format
  PEs pipelined to handle increased logic requirements
Single Instruction Multiple Data (SIMD) processing
  Each PE can process two instructions per cycle

## Slide 11: Overall results

## Slide 12: Assessing Performance – v1 vs. v1.5 vs. v2
Eyeriss v1 retains original architecture but scaled to match v1.5 and v2 specs (storage capacity, number of PEs, and data precision)

## Slide 13
Comparative results

## Slide 14
Comparative results

## Slide 15
Comparative results
Layer-by-Layer Latency of Sparse AlexNet on Eyeriss v2 vs. v1

## Slide 16: Comparisons to other designs
Similar amount of resources with significantly fewer MACs
Logic to process sparsity
Achieves comparable throughput & energy efficiency

## Slide 17: Conclusion
Flexibility & Efficiency
Reconfigurable with programmable PEs
Support for many DNN models & layer types
Memory Management
Hierarchical on-chip memory network
Buffers to reduce off-chip access
Minimizes energy consumption, maximizes data reuse
Support for Sparsity
Reduces model size and increases performance
Scalability
Configurable number of PEs for variable throughput
Energy and performance modes
Incredibly Promising for Edge Computing

## Slide 18: The END
Q/A

## Slide 19: THANK You
Niko Pedraza
nikopedraza@u.boisestate.edu
Carson Keller
carsonkeller@u.boisestate.edu
Adam Torek
adamtorek@u.boisestate.edu